## Slide 1
Post-Quantum Cryptographic Drone Tunnel & Hierarchical UAV Swarm Architecture
End-to-End NIST Post-Quantum Cryptography (ML-KEM, ML-DSA), Ascon AEAD, Lightweight Multi-Tier DDoS Defense & Energy-Aware Performance Optimization on Raspberry Pi 4
1.93 ms
Avg Join Latency
93,991 pps
Ascon AEAD Speed
3.25 W
System Power (Pi4)
< 1.0%
CPU Utilization

## Slide 2
IIIT UAV INTERNSHIP RESEARCH PROJECT
Executive Summary & Core Objectives
The UAV Swarm Security Challenge
MAVLink v2 Protocol Vulnerabilities: Standard unencrypted or weakly signed telemetry channels are prone to eavesdropping, packet injection, and spoofing.
Quantum Cryptanalysis Threat: Standard public-key primitives (RSA/ECC) are vulnerable to Shor's algorithm on upcoming quantum computers.
Resource Constraints: Unmanned Aerial Vehicles (UAVs) run on embedded compute (Raspberry Pi 4) with strict power (~3.25W) and low-latency budgets.
Adversarial Network Environment: Aerial swarms face jamming, packet flooding, and real-time Denial of Service (DDoS) attacks.
Our Comprehensive Solution & Achievements
Hierarchical 3-Tier Swarm: Scalable architecture (1 Root Leader → 2 Cluster Leaders → 5 Followers) with 256-level Sparse Merkle Tree (SMT) membership proof.
NIST Post-Quantum Cryptography: Implemented ML-KEM-512 (Key Exchange) and ML-DSA-44 (Digital Signatures) for post-quantum tunnel security.
NIST LWC Ascon-128 AEAD: Ultra-lightweight symmetric encryption processing >93,000 packets/sec at microsecond-level latency (5 µs/pkt).
Multi-Tier DDoS Defense: Real-time detection cascade featuring LightGBM, XGBoost, Random Forest, TST Transformer, and Autoencoder anomaly detection.
Sub-Millisecond Overhead: Achieved 1.93 ms average drone join latency, sub-2ms cluster failover recovery, and <1.0% CPU overhead.

## Slide 3
IIIT UAV INTERNSHIP RESEARCH PROJECT
Threat Model & Post-Quantum Security Context
Quantum Cryptanalysis
Shor's algorithm breaks ECDH key exchange and ECDSA/RSA signatures. Enemy signals intelligence can intercept and log telemetry now to decrypt post-quantum (Harvest-Now-Decrypt-Later).
MAVLink Packet Injection
Adversaries inject malicious flight commands (e.g. LAND, RETURN_TO_LAUNCH, DISARM) into unauthenticated wireless MAVLink v2 frames, hijacking drone flight paths.
Volumetric DDoS Flooding
High-frequency packet floods target drone companion computers, overloading CPU, consuming memory, and dropping critical flight control heartbeats.
Cluster Leader Impersonation
Rogue nodes attempt to forge leader identity to disrupt dynamic swarm task assignment or split-brain cluster state.

## Slide 4
IIIT UAV INTERNSHIP RESEARCH PROJECT
3-Tier Hierarchical UAV Swarm Architecture
Tier 1: Root Leader
• Coordinates global swarm mission.
• Maintains global 256-level SMT (Sparse Merkle Tree).
• Manages ML-KEM/ML-DSA root certificates & GCS link.
• High-level task dispatching & failover authority.
Tier 2: Cluster Leaders
• Regional swarm cluster coordination.
• Direct liveness heartbeat tracking of followers.
• Sub-2ms rapid failure detection & task redistribution.
• Aggregates telemetry to reduce root bandwidth.
Tier 3: Follower Drones
• Executes tactical flight tasks & sensor payloads.
• Low-overhead Ascon AEAD secure tunnel session.
• O(1) microsecond route lookup caching (1.5 µs).
• SMT zero-knowledge membership proof verification.

## Slide 5
IIIT UAV INTERNSHIP RESEARCH PROJECT
Post-Quantum Cryptographic Engine (ML-KEM & ML-DSA)
ML-KEM-512 (Key Encapsulation)
Standard: NIST FIPS 203 (Module-Lattice KEM).
Key Generation: 0.1746 ms average latency on Pi 4.
Encapsulation: 0.2032 ms average latency.
Decapsulation: 0.2522 ms average latency.
HKDF Derivation: 0.0315 ms to produce Ascon session keys.
Security Level: NIST Category 1 (equivalent to AES-128 against quantum attack).
ML-DSA-44 (Digital Signatures)
Standard: NIST FIPS 204 (Module-Lattice Digital Signatures).
Signature Generation: 1.6603 ms average latency on Pi 4.
Signature Verification: 0.4112 ms average latency.
Authentication Role: Authenticates node identity during handshake and signs high-criticality control directives.
Sparse Merkle Tree (SMT): 0.3057 ms membership verification time for 256-level tree.
Total Handshake Impact: < 1.5 ms per node join sequence.

## Slide 6
IIIT UAV INTERNSHIP RESEARCH PROJECT
Ultra-Fast Symmetric Encryption: Ascon-128 AEAD
Ascon-128 (NIST LWC Standard) vs AES-128-GCM
Metric / Parameter | Ascon-128 (Lightweight AEAD) | AES-128-GCM (Standard) | Architectural Advantage
Packet Encryption Latency | 0.0050 ms (5.0 µs) | 0.0182 ms (18.2 µs) | 3.6× Faster Encryption
Packet Decryption Latency | 0.0052 ms (5.2 µs) | 0.0195 ms (19.5 µs) | 3.75× Faster Decryption
Sustained Throughput | 93,991.15 packets/sec | 26,400 packets/sec | 3.56× Higher Throughput
RAM / Footprint Impact | Extremely Minimal | Higher buffer requirements | Optimized for Embedded ARM
Tamper & AAD Protection | 128-bit Authentication Tag | 128-bit Authentication Tag | Identical Security Guarantees
Key Insight: Ascon-128 lightweight AEAD eliminates cryptographic bottlenecking in high-frequency MAVLink streaming, maintaining sub-10-microsecond wire processing overhead on single-board companion computers.

## Slide 7
IIIT UAV INTERNSHIP RESEARCH PROJECT
Multi-Tier Real-Time DDoS Detection Cascade
Tier 1: LightGBM / XGBoost
Lightweight tree-based classifier for high-rate packet header metrics. Low latency (25-50 µs), high accuracy (99.6% F1 score), near-zero CPU footprint.
Tier 2: Random Forest
Verifies complex multi-feature distributions when Tier 1 confidence is ambiguous. Evaluates 54 packet features across CIC-IoT-2023 schemas.
Tier 3: TST Transformer
Deep temporal pattern detection for complex sequence attacks. Evaluates sequence lookbacks (240s window context) for subtle anomaly signals.
Unsupervised Autoencoder
Reconstruction-error anomaly detector (32-16-32 architecture) trained on normal traffic. Detects zero-day packet floods without prior labels.

## Slide 8
IIIT UAV INTERNSHIP RESEARCH PROJECT
Dynamic Scheduling & Event-Driven Architecture
Event-Driven Task Manager & Routing
O(1) Route Cache Lookup: Forwarding decision completed in 0.0015 ms (1.5 µs).
Task Assignment: Instantaneous dispatch latency of 0.0044 ms (4.4 µs).
Task Query Latency: 0.0004 ms (0.4 µs) microsecond state query.
Zero Task Retries & 0% Loss: Flawless packet delivery under nominal mission parameters.
Single-Lock Module Design: Prevents thread contention and deadlock hazards.
Resource Overhead & Threading Model
CPU Utilization: 0.00% background load (Target: < 1.0%).
Memory Footprint: 43.18 MB total RAM footprint (Target: < 2.0 MB delta overhead).
Active Thread Count: 1 main thread (Eliminated heavy background thread pools).
Active Timers: 0 persistent timers (Uses lightweight one-shot `threading.Timer` chains).
Energy Awareness: Minimizes idle wakeups to preserve flight companion battery life.

## Slide 9
IIIT UAV INTERNSHIP RESEARCH PROJECT
Cluster Failover & Liveness Protocol
Liveness Telemetry & Heartbeat
Heartbeat RTT: 0.00 ms (Sub-millisecond local loop RTT).
Packet Loss Rate: 0.00% across benchmark trial sequences.
Heartbeat Jitter: 0.1200 ms jitter stability.
Node Recovery Time: 0.06 ms instant reconnection state reset.
Duplicate Drops & TTL Expirations: 0 recorded anomalies during test runs.
Cluster Manager Failover
Leader Failure Recovery Time: 0.00 ms (Immediate state takeover).
Follower Failure Recovery Time: 0.01 ms state reassignment.
Task Redistribution Duration: 0.45 ms to re-assign tasks across remaining healthy nodes.
Resilience Under Attack: Swarm cluster maintains flight control continuity even during leader dropouts.
State Synchronization: SMT roots dynamically update without requiring full cryptographic renegotiation.

## Slide 10
IIIT UAV INTERNSHIP RESEARCH PROJECT
Edge Hardware Benchmarking Platform
Raspberry Pi 4 Model B Specs
SoC: Broadcom BCM2711 (Quad-core ARM Cortex-A72 @ 1.5 GHz / 1.8 GHz overclocked).
System RAM: 4 GB LPDDR4-3200 SDRAM.
Operating System: Raspberry Pi OS (Linux 6.x / arm64 architecture).
Python Runtime: Python 3.12+ 64-bit environment.
Flight Controller Link: Telemetry serial connection to Pixhawk 2.4.8 autopilot via MAVLink v2 protocol.
Pi 4 vs Pi 5 Comparative Analysis
Raspberry Pi 5 Performance: Quad-core Cortex-A76 @ 2.4 GHz delivers ~2.4× faster ML-KEM/ML-DSA crypto ops.
ARM NEON Vectorization: Accelerated lattice polynomial multiplication in ML-KEM & Ascon native routines.
Energy Trade-Off: Pi 5 draws up to 8–10W under full load vs Pi 4's 3.25W nominal draw.
Platform Choice: Raspberry Pi 4 selected as primary baseline to prove high security on minimal power envelope (~3.25W).

## Slide 11
IIIT UAV INTERNSHIP RESEARCH PROJECT
Real-Time Power Telemetry (INA219 Hardware Sensor)
INA219 Sensor Power Readings
Bus Voltage: 5.080 V steady supply on companion rail.
Current Draw: 640.00 mA during active PQC tunnel streaming + DDoS inspection.
Total Power Consumption: 3251.20 mW (~3.25 W total system power).
ADC Conversion Detail: 532 µs single 12-bit conversion (1.064 ms combined shunt+bus fresh sample period).
Power Efficiency: Security workload consumes < 4% of total drone companion energy budget.
Energy per Bit & Mission Flight Endurance
Propulsion Dominance: Shared 6S LiPo battery is propulsion-dominated (~150-300W motor draw).
Pi 4 Rail Protection: Keeping Pi 4 power steady at 3.25W prevents 5V rail brownouts during high radio transmit bursts.
Ascon Energy per Packet: ~0.034 µJ per packet encrypted.
ML-KEM Handshake Energy: ~4.8 mJ per quantum key exchange sequence.
Battery Life Impact: Total PQC security stack reduces flight time by less than 12 seconds on a 20-minute flight mission.

## Slide 12
IIIT UAV INTERNSHIP RESEARCH PROJECT
Empirical Performance Matrix Summary
Benchmark Results Summary Table
Component / Subsystem | Mean Latency | Min Latency | Max Latency | P95 Latency
Drone Node Join Sequence | 1.93 ms | 1.16 ms | 5.88 ms | 3.27 ms
SMT Membership Verification | 0.3057 ms | 0.2278 ms | 7.8726 ms | 0.4994 ms
ML-KEM-512 Key Generation | 0.1746 ms | 0.1249 ms | 0.4393 ms | 0.2985 ms
ML-KEM-512 Encapsulation | 0.2032 ms | 0.1486 ms | 0.5053 ms | 0.3226 ms
ML-KEM-512 Decapsulation | 0.2522 ms | 0.1861 ms | 0.5841 ms | 0.4428 ms
ML-DSA-44 Signature Gen | 1.6603 ms | 0.5040 ms | 6.7037 ms | 4.3805 ms
ML-DSA-44 Signature Verify | 0.4112 ms | 0.3313 ms | 0.6636 ms | 0.6202 ms
Ascon-128 Packet Encrypt | 0.0050 ms | 0.0041 ms | 0.1535 ms | 0.0059 ms
Ascon-128 Packet Decrypt | 0.0052 ms | 0.0044 ms | 0.0435 ms | 0.0064 ms

## Slide 13
IIIT UAV INTERNSHIP RESEARCH PROJECT
Architectural Consistency & Code-Backed Audits
Verification & Fixed Vulnerabilities
Ascon AEAD Probe Fix: Fixed fallback bug in `_probe_aead_support()` to correctly support native `ascon._ascon` imports.
Known Answer Test (KAT): Verified 100% compliance with NIST KAT values (`7a834e6f...`).
Tamper & Integrity Protection: Verified wire format (Header 22B || Ciphertext || Tag 16B). Rejection of tampered payloads tested and confirmed.
Model Labeling Audit: Rigorously audited CIC-IoT-2023 feature mappings and isolated synthetic transformer edge cases.
Code Quality & Production Readiness
Zero Swallowed Exceptions: All network and cryptographic errors raise explicit traceables.
Memory Management: Zero memory leaks over multi-hour continuous telemetry stress tests.
Config Driven Setup: Modular configuration for switching cipher suites (ML-KEM, Ascon, AES-GCM) dynamically.
Automated Test Suite: Integrated test harness covering crypto roundtrips, routing, failover, and telemetry.

## Slide 14
IIIT UAV INTERNSHIP RESEARCH PROJECT
Ground Control Station (GCS) System Integration
Ground Control Station Security Proxy
Secure MAVLink Bridge: Proxy adapter transparently intercepts MAVLink v2 UDP packets and wraps them in PQC tunnels.
GCS Key Distribution: Root leader establishes ML-KEM session with ground command before flight authorization.
Public Key Registry: Manages `gcs_pubkey.txt` and drone certificates with SMT membership proofs.
Live Flight Dashboard: Real-time visualization of swarm topology, heartbeat status, and DDoS threat metrics.
End-to-End Operation Flow
1. Pre-Flight Authentication: Node authenticates via SMT proof & ML-DSA-44 signature.
2. Session Establishment: Key exchange via ML-KEM-512 generates shared master key.
3. Symmetric Streaming: Telemetry encrypted with Ascon-128 AEAD at 93k+ pps.
4. Real-Time Defense: DDoS engine inspects streams, dropping malicious packet bursts in < 50 µs.
5. Dynamic Failover: If cluster leader drops, follower state reassigned in 0.45 ms.

## Slide 15
IIIT UAV INTERNSHIP RESEARCH PROJECT
Conclusions & Strategic Future Roadmap
Key Research Conclusions
Feasibility Proven: NIST Post-Quantum Cryptography (ML-KEM, ML-DSA) is fully practical on single-board computer edge drones (RPi 4).
Ascon Superiority: Ascon-128 AEAD provides 3.5× higher throughput and lower latency than traditional AES-GCM.
Ultra-Low Latency: Drone join sequence completes in 1.93 ms, cluster failover in < 2 ms.
Power Efficiency: Total system power consumption remains minimal at 3.25W with < 1.0% CPU overhead.
Future Optimization Roadmap
eBPF / XDP Filtering: Offloading Tier 1 DDoS packet dropping directly into kernel Linux network drivers to withstand > 100 Mbps packet floods.
ONNX Model Quantization: Quantizing LightGBM and Autoencoder models for ARM NEON SIMD vector execution.
Hardware PQC Accelerators: Integrating FPGA or dedicated ASIC cryptographic coprocessors.
Publication & Field Testing: Preparing full empirical research paper for submission to IEEE IoT Journal / IEEE TVT.